## Slide 1
DEEPGRID SEMI · SOVEREIGN FOUNDRY MIGRATION ROADMAP
One Method, Three Factories Sovereignty & Foundry Portability
SkyWater (USA) Prototyping -> IHP (Germany) 77 GHz Radar -> SCL Mohali (India) Buy(Indian-IDDM) Defence Lock-in.
FACTORY 1: PROVEN
SkyWater 130nm (USA) Validated Silicon on MPW
FACTORY 2: DIFFERENTIATED
IHP SG13G2 SiGe (Germany) 350 GHz fT mmWave Radar
FACTORY 3: SOVEREIGN
SCL Mohali 180nm (India) 100% Domestic IDDM Defense Fab
PORTING BOUNDARY
Scripted Digital (.lib) Manual Analog Recalibration

## Slide 2
GEOPOLITICAL SILICON DILEMMA
The $9B Mature-Node Import Trap Demands Multi-Factory Portability
Relying solely on foreign fabs risks export embargoes, while waiting for domestic fab modernization stalls commercial traction.
1. Foreign Fab Single-Sourcing Risk
• India imports $9B in mature-node chips (130nm–180nm) powering defense and aerospace.
• Western fabs are bound by ITAR and potential sudden export license revocations.
• Taiwanese fabs (TSMC/UMC) face severe geopolitical disruption risks across the Taiwan Strait.
• Indian military programs cannot build sovereign defense on fragile foreign silicon.
2. The Domestic Fab Reality (SCL)
• Semi-Conductor Laboratory (SCL) Mohali operates an operational 180nm CMOS/BCD line.
• However, prototyping every early digital experiment solely at SCL slows iteration cycles.
• Commercial fabless teams need fast, low-cost tapeouts to validate digital RTL quickly.
• The answer is a sequential bridge: prove digital IP globally, transfer sovereignty domestically.
3. The DeepGrid 3-Factory Thesis
• One standardized open-source design flow (OpenLane / Yosys / OpenROAD).
• Factory 1 (SkyWater): Fast, $14.3K MPW digital proof of silicon.
• Factory 2 (IHP Germany): World-class 350 GHz SiGe for 77 GHz radar.
• Factory 3 (SCL Mohali): Complete sovereign defense lock-in under DAP-2020 Make-II.

## Slide 3
THE THREE FOUNDRIES COMPARED
Distinct Roles Across Prototyping, High-Frequency Radar, And Sovereign Defense
Each foundry serves a specific economic and physical purpose in DeepGrid's long-term silicon compounding model.
1. SkyWater SKY130 (USA)
FOUNDRY STATUS: PROVEN (DONE)
• Node: 130 nm Planar CMOS (5-Metal Stack).
• Status: PROVEN SILICON — Physical working test chips fabricated & validated.
• Cost: $14,300 per MPW shuttle run; eliminates $1M EDA tool tax.
• Procurement: Qualifies as DAP-2020 Buy (Indian) since RTL is Indian-owned.
• Primary Role: Rapid commercial prototyping & digital processor IP proof.
2. IHP Leibniz SG13G2 (Germany)
FOUNDRY STATUS: DIFFERENTIATED
• Node: 130 nm SiGe:C BiCMOS Heterojunction Bipolar.
• Transistor Physics: Ultra-high speed fT = 350 GHz, fmax = 450 GHz.
• Status: PLANNED — Target tapeout for SKU-7 77 GHz MIMO Radar.
• Aerospace Profile: DO-160G airborne qualified high-frequency RF front-end.
• Primary Role: 4D mmWave radar for drone & automotive collision avoidance.
3. SCL Mohali (India)
FOUNDRY STATUS: SOVEREIGN DEFENCE
• Node: 180 nm Military-Qualified CMOS & High-Voltage BCD.
• Status: STRATEGIC TRANSFER — Dedicated domestic defense manufacturing.
• Procurement: Unlocks DAP-2020 Buy (Indian-IDDM) absolute monopoly status.
• Sovereignty: 100% domestic IP, fab, assembly, and test immune to sanctions.
• Primary Role: Sovereign military production for Indian Army, BEL, and DRDO.

## Slide 4
THE HONEST PORTING BOUNDARY
Digital Logic Moves By Script; Analog Circuits Require Physical Re-Engineering
DeepGrid rejects false marketing claims of 'instant zero-cost analog migration': physics dictates the real engineering boundary.
PORTABLE VIA SCRIPTING (AUTOMATED)
FOUNDRY STATUS: DIGITAL LOGIC
• Verilog / SystemVerilog digital RTL codebases and synthesizable modules.
• DGridRiscV processor core architecture (RV32IM_Safety).
• AXI4 crossbar interconnect matrices, arbiters, and FIFO buffers.
• UVM verification testbenches, assertions, and coverage closure plans.
• Porting Mechanism: Automated Liberty (.lib) timing file swap + OpenROAD re-run.
• Engineering Overhead: <2 weeks of scripted timing closure per foundry retarget.
REQUIRES MANUAL RE-ENGINEERING (PHYSICS-BOUND)
FOUNDRY STATUS: ANALOG & BCD
• Bandgap Voltage References: Brokaw cells require resistor trimming for 12 ppm/°C.
• High-Voltage BCD Output Stages: 5V–120V LDMOS doping profiles differ per foundry.
• Foundry Non-Volatile Memory (NVM / OTP / EEPROM): Proprietary hard macros.
• ESD / EOS Pad Protection Rings: Must be redrawn and sized to meet ±15 kV HBM.
• Porting Mechanism: 1 to 2 dedicated calibration shuttle cycles per new foundry node.
• Engineering Overhead: 6–9 months of physical layout and silicon characterization.

## Slide 5
OPEN-SOURCE EDA PORTABILITY
OpenLane, Yosys, And OpenROAD Slashes NRE And Enables Frictionless Retargeting
Automated physical design flow removes the multi-million-dollar tool barrier and locks IP into reproducible scripts.
1. Zero Tooling License Tax
• Proprietary EDA tool suites (Synopsys, Cadence) cost $1M–$2M per tapeout.
• DeepGrid's physical design operates 100% on open-source Yosys and OpenROAD.
• Eliminates per-seat licensing costs and legal export approval from US EDA vendors.
• Complete GDSII generation executes on local workstations in Hyderabad.
2. Automated Liberty (.lib) Swap
• When moving from SkyWater to SCL Mohali, the digital RTL remains completely untouched.
• Tool scripts swap target technology LEF files and standard-cell timing libraries (.lib).
• Floorplanning, clock-tree synthesis (CTS), and global routing execute deterministically.
• Guarantees timing closure at target clock boundaries (200 MHz fixed).
3. Fast Shuttle Compounding
• Multi-Project Wafer (MPW) shuttles allow rapid silicon validation at $14.3K per run.
• DeepGrid executes a complete design-to-silicon shuttle loop every 198 days.
• Validates 1,000 silicon-tested building blocks that compound into 50 approved SKUs.
• De-risks complex SoC subsystems before committing to volume SCL production.

## Slide 6
DEFENCE PROCUREMENT LAW MOAT
Buy (Indian-IDDM) Grants Unconditional Monopoly Priority In Indian Defence Tenders
Foreign chipmakers (TI, STMicro, ADI) are legally excluded from top-tier sovereign military procurement.
1. Buy (Indian) vs Buy (Indian-IDDM)
• DAP-2020 establishes a rigid legal hierarchy for all Indian military procurement.
• SkyWater & IHP silicon qualifies as Buy (Indian) because design & IP are 100% Indian.
• SCL Mohali silicon unlocks Buy (Indian-IDDM): Indigenously Designed, Developed & Manufactured.
• Buy (Indian-IDDM) holds mandatory statutory priority over all other procurement tiers.
2. Positive Indigenisation Lists (PIL)
• Ministry of Defence (MoD) has notified 5 Positive Indigenisation Lists banning imports.
• Covers drone flight controllers, high-reliability PMICs, and tactical communications ICs.
• Foreign suppliers cannot bid once a verified domestic IDDM alternative exists.
• Guarantees a legally protected domestic market for DeepGrid's mature-node SKUs.
3. SCL Mohali Sovereign Lock-in
• Domestic fabrication at SCL Mohali makes DeepGrid products completely sanction-proof.
• Zero ITAR dependencies; immune to US, European, or Chinese geopolitical embargoes.
• Secures long-term 15-to-20-year defense program availability.
• Establishes DeepGrid as the default semiconductor provider to BEL, DRDO, and MCEME.

## Slide 7
POST-SILICON PRODUCTIZATION
Fabrication Is Step One: Packaging, ATE Screening, And Qualification In Hyderabad
DeepGrid completes the semiconductor loop with in-house automated test equipment and domestic multi-die packaging.
1. Multi-Die Organic SiP Packaging
• Standard 4-layer organic laminate substrate (FR4/BT core) BGA packaging.
• Composes mature dies from SkyWater, IHP, and SCL into a single rugged module.
• Deliberately rejects expensive UCIe / TSMC CoWoS silicon interposers.
• Packaging NRE under $35,000 with >99% assembly yield across domestic ATMP lines.
2. Dedicated ₹1.2 Cr ATE Testing Line
• High-throughput automated test equipment (ATE) production line in Hyderabad.
• Automated wafer probe testing to ensure Known Good Die (KGD) before SiP assembly.
• Thermal chamber screening across full aerospace range (-55°C to +125°C).
• Eliminates reliance on foreign test houses and preserves design IP security.
3. Military Environmental Qualification
• MIL-STD-883K: High/low temperature cycling, thermal shock, and hermetic seal tests.
• MIL-STD-461G: Radiated emissions and electromagnetic interference shielding.
• CEMILAC and JSS-55555 airworthiness certification for frontline defense flight.
• Pre-ASIC live orders (MCEME ₹1.01 Cr, Infinis, Axitech) validate field reliability.

## Slide 8
10-SKU FOUNDRY ALLOCATION MATRIX
Matching Each Semiconductor SKU To Its Optimal Foundry Physics And Procurement Path
Every chip in DeepGrid's portfolio is mapped to a specific process node based on voltage, frequency, and market sovereignty.
SKU-1: BLDC MOTOR CONTROLLER
SkyWater 130nm BCD -> SCL 180nm BCD
5–120V Rail, FOC CORDIC PID (<1 µs), BEE 5-Star Fans & EV 2-Wheelers
SKU-2: SMART METER SOC
SkyWater 130nm CMOS -> SCL 180nm CMOS
24-bit Sigma-Delta ADC, <2 µW RTC, 250M National Smart Meter Rollout
SKU-3: HI-REL PMIC (28V)
SCL Mohali 180nm BCD / SkyWater
Brokaw Bandgap (12 ppm/°C), DICE FSM, DO-160 & SRIJAN Defense Power
SKU-4: LOCKSTEP SAFETY MCU
SkyWater 130nm -> SCL 180nm
Dual DGridRiscV with 2-Cycle Skew, ISO 26262 ASIL-D, <=2-cycle FAULTn
SKU-5: INTERFACE TRANSCEIVER
SkyWater 130nm Thick-Oxide HV
5V LDMOS, CAN-FD (5 Mbps), RS-485, ±15 kV HBM ESD Protection
SKU-6: VOLTAGE SUPERVISOR
SCL Mohali 180nm / SkyWater
Chopper-Stabilized Reference, 8 µs Deglitch, MIL-STD-883 Pathfinder
SKU-7: 77GHZ MIMO RADAR
IHP Leibniz SG13G2 (Germany)
SiGe:C BiCMOS 350 GHz fT, 3.75 cm Distance Res, 4D Imaging Automotive ADAS
SKU-8: RUGGED DISPLAY DRIVER
SkyWater 130nm HV -> SCL 180nm
0–12V Column Amps, 1280x10b DACs, BEL 17" Rugged SXGA, PIL-5 Item #5
SKU-9: SDV ZONAL GATEWAY
SkyWater 130nm + SCL 180nm BCD
16x Smart Solid-State e-Fuses, Gigabit TSN Switch, 4x CAN-XL (20 Mbps)
TRACK B: D100 DRONE SOC
SkyWater 130nm + 28nm Compute SiP
Dual DGridRiscV Flight Loop + 30 Hz EKF VIO + Isolated Hardware Failsafe

## Slide 9
SEQUENTIAL MIGRATION TIMELINE
De-Risking Execution: Commercial Validation Precedes Domestic Defence Fab Transfer
A disciplined, phased execution model ensures revenue generation begins while long-cycle military qualification matures.
Stage 1: Commercial Shuttles (Months 1–12)
FOUNDRY STATUS: PHASE 1: PROTOTYPE
• Fabricate digital test chips on SkyWater 130nm MPW shuttles (CI2609 & CI2612).
• Validate DGridRiscV core and basic analog macros in physical silicon.
• Fulfill live commercial pilot orders with MCEME (₹1.01 Cr), Infinis, and Axitech.
• Establish automated testing scripts and baseline yield metrics in Hyderabad.
Stage 2: Radar & High-Frequency (Months 10–24)
FOUNDRY STATUS: PHASE 2: DIFFERENTIATION
• Execute IHP SG13G2 SiGe BiCMOS radar front-end tapeout (SKU-7).
• Validate 77 GHz mmWave transceivers and 4D imaging MIMO antennas.
• Assemble multi-die packaging prototypes combining digital compute with radar die.
• Initiate automotive Tier-1 ADAS pilots and airborne UAV integration.
Stage 3: SCL Mohali Defense Transfer (Months 18–36)
FOUNDRY STATUS: PHASE 3: SOVEREIGN MONOPOLY
• Transfer validated RTL and re-engineer analog BCD macros for SCL 180nm fab line.
• Run initial pilot qualification shuttles at SCL Mohali under Make-II program.
• Achieve formal Buy (Indian-IDDM) certification and Approved Vendor List (AVL) inclusion.
• Scale to full multi-thousand-unit production for Indian armed forces.

## Slide 10
FINANCIAL MODEL & CAPITAL EFFICIENCY
How ₹10 Cr In Capital Unlocks A ₹1,000 Cr Sovereign Semiconductor Business
Capital allocation breakdown, Chinese price crash insulation, and the FY31 sovereign revenue buildup.
USE OF ₹10 CR FUNDS
Precision Allocation
• ₹3.6 Cr: Foundry fabrication and MPW shuttles across SkyWater, IHP, and SCL.
• ₹2.4 Cr: Core engineering team (12 senior physical design & analog IC engineers).
• ₹1.8 Cr: Defense environmental qualification (MIL-STD-883, JSS-55555, CEMILAC).
• ₹1.2 Cr: Dedicated ATE testing line & probe station in Hyderabad.
CRASH RESILIENCE
Stop Rules S1–S4
• Stress-tested against a 50% Chinese mature-node price dumping crash.
• Gross margin remains resilient at 58% under extreme price competition.
• Domestic defense buyers legally cannot buy Chinese silicon under PIL rules.
• Strict stop rules enforce financial discipline before each tapeout commitment.
SOVEREIGN MONOPOLY
DAP-2020 Make-II
• Buy(Indian-IDDM) creates statutory insulation: foreign bids excluded by law.
• Indian Army MCEME, BEL, and ideaForge anchor demand guarantees off-take.
• Pre-ASIC contracted traction (₹2.88 Cr) proves demand before volume fab.
• High customer switching costs once design is frozen into military avionics.
REVENUE BUILDUP
₹1,000 Cr by FY31
• FY27: ₹12 Cr (Commercial pilots & initial defense delivery).
• FY28: ₹65 Cr (Volume drone SoCs & smart meter rollouts).
• FY29: ₹240 Cr (Automotive zonal controllers & radar adoption).
• FY31: ₹1,000 Cr+ across 50 mature building blocks powering 10 SKUs.