## Slide 1
DEEPGRID SEMI · DG32-2DOM · PRELIMINARY DATASHEET
DG32-2DOM: DG32-LITE plus one engine
What the DG32-2DOM preliminary datasheet adds and what it leaves unchanged · design values, process nominals and analytic estimates, each labelled
TWO CLOCK DOMAINS · ILLUSTRATIVE
0
PADS ADDED
114 MHz
ENGINE CLOCK
400
KEYS PER HEAD
QFN-64
SAME PACKAGE
Preliminary, pre-silicon. Register offsets, the memory map and board-design rules are in the engineering datasheet, not this deck.
DEEPGRID SEMI · DG32-2DOM PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
01
Notes: DG32-2DOM is the attention variant of DG32-LITE, and its preliminary datasheet reads like DG32-LITE's with one addition: an INT8 attention engine on its own clock. This deck covers what the datasheet adds, and confirms what it leaves unchanged. Every figure is a design value, a process nominal or an analytic estimate, and each is labelled.

## Slide 2
02 · EXECUTIVE SUMMARY
Same pins, same rails, one added clock
DG32-2DOM against DG32-LITE, in the four numbers a design checks first
DEEPGRID SEMI · DG32-2DOM PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
02
64 / 44
PINS / SIGNALS
Identical to DG32-LITE
1.8 / 3.3 V
CORE / I/O
Identical rails and limits
50 + 114
MHZ CLOCKS
CPU domain + engine domain
~3,242
CYCLES PER ROW
Analytic, at 16 lanes
Board
Identical footprint, pin map, rails and boot flash.
Firmware
One memory-mapped engine, programmed in four steps.
Limits
400 keys, 64-byte values, ~3,242 cycles per row.
For a board, DG32-2DOM is a drop-in DG32-LITE. For firmware, it adds one memory-mapped engine that runs on its own clock and never stalls the control core.
Source: DG32-2DOM preliminary datasheet §1, §2, §4, §6.1.
Notes: If you have designed with DG32-LITE, most of this is already familiar. The package, the sixty-four pins and the forty-four signals do not move, and neither do the one point eight and three point three volt supplies. What is new is a second clock at one hundred fourteen megahertz, driving the engine beside the fifty megahertz CPU. A board designer sees the same chip; only the firmware sees something extra.

## Slide 3
03 · WHAT IS NEW
Five datasheet features are new in DG32-2DOM
Everything else in the feature list is DG32-LITE’s, unchanged
DEEPGRID SEMI · DG32-2DOM PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
03
NEW FEATURE
WHAT THE DATASHEET STATES
Attention accelerator
One kick computes a band of query rows of one head, end to end, bit-exact to the golden model
Shared datapath
One multiply array across lanes, a 256-entry 15-bit weight table and a 40-bit numerator exact to 131,072 keys
Row cost
~3,242 cycles per query row, analytic, at 16 lanes
Second clock domain
The engine runs at 114 MHz and crosses to the 50 MHz CPU through two-flop bridges
Its own die
3.4 × 4.5 mm, with key and value buffers on SRAM macros beside the analog corner
The engine is internal: it reaches memory over the on-chip bus and takes commands from the CPU through its register port.
Source: DG32-2DOM preliminary datasheet §1 features.
Notes: Only five entries in the feature list are new, and all of them exist because of the engine. It computes a whole span of rows for an attention head each time it is started, and its results match the reference software exactly. One shared multiplier and a small weight table keep that hardware compact. Each row costs about thirty-two hundred cycles by analysis. And the engine brings its own faster clock, plus a larger die to hold its buffers.

## Slide 4
04 · WHAT IS UNCHANGED
Pins, rails and limits are unchanged
Section by section against the DG32-LITE preliminary datasheet
DEEPGRID SEMI · DG32-2DOM PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
04
DATASHEET SECTION
DG32-LITE
DG32-2DOM
Package
QFN-64, 9 × 9 mm, 0.5 mm pitch
Identical
Signal pins
44 in eleven groups
Identical; the engine adds no pads
Core / I/O rails
1.8 V (1.71–1.89) / 3.3 V (3.0–3.6)
Identical
Absolute maximums
vccd1 1.95 V, vddio 3.63 V
Identical
Power estimate
~0.43 W at 50 MHz, tool estimate
Same figure repeated; no separate engine figure stated
Boot flow
Self-boot from QSPI flash, UART monitor fallback
Identical
Clocks
One 50 MHz domain
50 MHz CPU + 114 MHz engine
Sources: DG32-2DOM preliminary datasheet §2–§6, §10; DG32-LITE preliminary datasheet.
Notes: Everything else is unchanged. The package, the pin groups, the rails and their limits, and the boot flow are identical to DG32-LITE, because the engine is internal and adds no pads. The datasheet repeats the same zero point four three watt estimate at fifty megahertz, and it does not yet state a separate figure for the engine.

## Slide 5
05 · CLOCKS
The engine runs on its own 114 MHz clock
Two domains on one die; the crossing is the only path between them
DEEPGRID SEMI · DG32-2DOM PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
05
50 MHz domain
CPU, bus and every peripheral
Clock bridges
Two-flop synchronised crossings
114 MHz domain
INT8 attention engine
Why a second clock
The CPU and peripherals stay at 50 MHz, so the control core’s timing is untouched.
Why it never stalls control
The engine reaches memory through the bridges, so it never stalls the control core.
+0.30 ns
SLACK AT 50 MHZ
Post-route
+0.19 ns
SLACK AT 114 MHZ
Post-route
3.4 × 4.5 mm
DIE
Engine buffers beside the analog corner
Source: DG32-2DOM preliminary datasheet §1, §6.1, §10.
Notes: Why give the engine a clock of its own? Speeding up the whole chip would push the lockstep core past its timing limit, so the processor, the bus and all of the peripherals stay at fifty megahertz while the engine runs at one hundred fourteen. The two sides meet only through synchronised bridges, which means the engine can never hold up control. After layout, both clocks meet timing with positive slack.

## Slide 6
06 · PROGRAMMING THE ENGINE
Firmware programs a kick in four steps
Concept level: the datasheet’s register map is not reproduced here
DEEPGRID SEMI · DG32-2DOM PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
06
Place buffers
Query, key, value and output locations
Set geometry
Rows, keys, key and value sizes
Start
Optionally reuse loaded buffers
Wait for done
Poll, or take the engine interrupt
Reuse between kicks
A skip-load option reuses the weight table, keys and values from the previous kick.
What it reports
Busy and done, plus a rejected geometry or an arithmetic overflow.
Memory-mapped
The engine sits on the CPU’s bus as one block and adds no pins.
The engine runs on the 114 MHz clock and reaches memory through the bridges, so the 50 MHz CPU keeps running.
Source: DG32-2DOM preliminary datasheet §8 engine notes and interrupt sources (concept only).
Notes: From firmware, running the engine takes four moves. Point it at the memory holding its inputs and where its results should go. Describe the shape of the job: how many rows and keys, and how wide each vector is. Start it, reusing anything still loaded from last time if that saves work. Then wait, by polling or with an interrupt. If the job is shaped wrongly or the arithmetic would overflow, the engine says so.

## Slide 7
07 · ENGINE LIMITS
Every engine limit is fixed in silicon
The geometry and arithmetic bounds firmware sizes a model against
DEEPGRID SEMI · DG32-2DOM PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
07
PARAMETER
RANGE
NOTE
Query rows per kick
1 – 65,535
A band of rows of one head
Keys per head
1 – 400
Maximum set when the die was built
Key dimension
Up to 32 bytes
A multiple of the lane count and of 4
Value dimension
Up to 64 bytes
A multiple of the lane count and of 4
Multiply lanes
16
Width of the shared multiply array
Weight table
256 entries, 15-bit
Softmax weights are never quantised
Numerator
40-bit
Exact to 131,072 keys
Cost per query row
~3,242 cycles
Analytic, at 16 lanes, 400 keys, 32- and 64-byte vectors
Source: DG32-2DOM preliminary datasheet §1 and §8 engine parameters.
Notes: The engine's limits are set in silicon, so a model has to fit them rather than the other way round. One start covers up to sixty-five thousand five hundred thirty-five query rows, and each head can hold up to four hundred keys. Keys can be thirty-two bytes wide and values sixty-four. Sixteen multiply lanes, a two-hundred-fifty-six entry weight table and a forty-bit numerator keep the result exact up to one hundred thirty-one thousand keys.

## Slide 8
08 · ON THE BOARD
A DG32-LITE board takes DG32-2DOM unchanged
The engine is internal, so the board sees the DG32-LITE footprint
DEEPGRID SEMI · DG32-2DOM PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
08
0
BOARD SIGNALS ADDED
The attention engine is internal to the die
Same footprint
QFN-64, 9 × 9 mm, with an identical pin map.
Same supplies
A 1.8 V core and a 3.3 V I/O ring, with the same sequencing.
Same boot
External QSPI flash and the console UART, as on DG32-LITE.
Status: design complete, in physical trials.
Sources: DG32-2DOM preliminary datasheet §2, §5, §6, §9; DG32-LITE investor block diagram (status).
Notes: For the board, nothing changes. The footprint, the pin map, the supplies and their sequencing, and the boot flash and console are the same as DG32-LITE. The engine adds no board signals at all. The chip's status is design complete, and in physical trials.

## Slide 9
09 · CLOSE
One footprint. Two chips.
Register offsets, the memory map and board-level rules live in the engineering datasheet, not in this overview.
THREE THINGS TO REMEMBER
1 · The board is a DG32-LITE board
Same package, pins, rails and boot flash; the engine adds no board signals.
2 · One engine on its own clock
A memory-mapped INT8 attention block at 114 MHz that cannot stall control.
3 · Limits already fixed
400 keys, 64-byte values and about 3,242 cycles per query row, by analysis.
DEEPGRID SEMI · DG32-2DOM PRELIMINARY DATASHEET
09
Notes: Here is what matters for a design team. Any board laid out for DG32-LITE already fits DG32-2DOM. The new engine runs from a separate, faster clock and can never hold up motor control. And its limits are settled today, at four hundred keys, values of sixty-four bytes and roughly thirty-two hundred cycles per row, by analysis. Real measurements arrive with first silicon.